## Slide 1
RD50 CMOS project – nov čip RD50-MPW2 pride ven julija, 4 upornosti
mi bomo merili E-TCT s pasivnimi pixli (diode)
dobro bi bilo, če bi lahko brali in merili E-TCT tudi z aktivnimi detektorji
(to bi se dalo z RD50-MPW2, ker je čip majhen in je PCB narejen tako, da je čip ob robu)
Za branje aktivnih pixlov na RD50-MPW2 bi rabili
CaRIBOu – dobimo pri UNI Geneva ~1400 CHF
Xilinx ZC706 evaluation board ~ 2500 USD
 A tole nabavimo?
HVCMOS

## Slide 2
Status RADMON za ITk

## Slide 3
Approximate locations confirmed, to early to specify exact locations:
1) strip barrel outer cylinder, z ~ 0, r ~ 1100 mm, one in each quadrant  confirmed
2) strip EC volume (r ~ 600 mm, z ~ 1600 mm in each quadrant, on side A and C)
  fixed on the blades of disk 1 or disk 2  confirmed
3) endcap side A and C (z > 3000 mm, r ~ 400 mm and r ~ 800 mm, one in each quadrant)
  at r ~ 800 mm strip PP1 volume, fixed on the outer side of the structural bulkhead  confirmed
  at lower r (~ 400 mm )  on the outer side of PP1 (see figure)  confirmed
Lokacije radmonov (28)

## Slide 4
Radiation Monitor Sensor Board (RMSB)
3 cm x 3 cm, 0.8 cm thick
ceramic (Al2O3) hybrid, connected to PCB frame with soldered wires
back side covered with resistive layer to heat the ceramics  stabilize temperature at 20°C
fixed in PEEK support for mechanical protection and air gap for insulation
Sensors on ITk RMSB:
3 RadFETs (TID)  need to qualify NurFET
3 diodes (NIEL)
1 temperature sensor (10 kOhm NTC)
example from ATLAS ID shown on photos
 make something very similar for the ITk
connector
or
pigtail

## Slide 5
Readout
ELMB, DAC  current sources, temp. stabilization, communication with DCS as in ATLAS ID
 ELMB DAC goes only up to 30 V
 30 V je premalo, da bi šli do zadosti visokih doz (1e15 in 100 kGy)
partly custom made: combination of ELMB (for ADC, communication with DCS) and
fully custom made
Current source:
0.1 and 1 mA current pulses
up to 100 V
0.1 s – 1 s long

## Slide 6
Switching
matrix
1
2
3
4
28
28 channel
Temperature
Control unit
ADC (ELMB?)
Current source
ATLAS DCS
in USA15
Tele kose naj bi mi naredili
Narejeno mora biti nekje do 2026
Pri ATLAS je vse delal ELMB
Za upgrade je problem, da bi rabili
Višje napetosti kot cca 30 V kar
Lahko dobimo iz DAC