## Slide 1
Preparations for LFoundry 150 nm RD50-MPW2 testing in Ljubljana
F9 weekly, 21.02.2020
Bojan Hiti, F9, Jozef Stefan Institute

## Slide 2: RD50 – MPW2
CMOS chip developed in the scope of RD50
  Chief designer E. Vilella (Liverpool)
  Not yet advanced to the level of ATLAS CMOS
Collaborating institutes
  Liverpool
  HEPHY Vienna
  University of Barcelona + IFAE
  CPPM
  FBK
  Sevilla
  Valencia
  Lancaster
  IJS starting to get involved in testing
We have tested MPW1 in Summer 2018 with Edge-TCT (Petja and Jernej)
  Irradiation campaign
  Early breakdown at cca 50 V
  MPW2 breaks down at 130 V (unirr.)

## Slide 3: RD50 – MPW2
III
I
Structures III – Edge-TCT diode (3x3)
  Measure acceptor removal
Structure I – active analog pixel matrix
  Interesting for Edge-TCT?

## Slide 4: RD50 MPW2 chip
Everything except Structures III is metalized on top
We will receive some chips already fully wire bonded and some bare chips (for Edge-TCT)
  In next two weeks
III
I
III
I

## Slide 5: Pixel structure

## Slide 6: Readout system
Readout system for readout of active devices (f.e. analog pixel matrix)
Xilinx ZC 706 commercial SoC developmnet board
CaRibou general purpose test board developed by Uni Geneva + BNL
Firmware developed by Vienna (engineer) – plug and play (SD card)
DAQ Software developed by Liverpool (PhD student) – GUI
  Runs on a Linux PC
Common code repository in CERN Gitlab being established

## Slide 7: Edge-TCT setup – active pixel matrix
ZC706
Caribou

## Slide 8: Sr90 setup
Sr90 setup is also available
Could be used for tests with analog matrix?

## Slide 9: Active pixels
Analog CSA output
Comparator output
To us not yet clear whether data can be recorded with Caribou directly to PC or an oscilloscope is required

## Slide 10: Active pixels
To us not yet clear whether data can be recorded with Caribou directly to PC or an oscilloscope is required

## Slide 11: Brainstorming
What are potential things to measure with the active matrix?
  Edge-TCT and Sr90 are possible
Running the DAQ requires Linux PC
  Option 1: install Virtual Machine on Windows PCs in the lab
  Option 2: use Intel NUC with Ubuntu and transfer it between setups